## Slide 2: Internet Of Things - Sessions
Arduino - Hello World
Introduction to Arduino
Blinking LED
Arduino - Advanced
Button and photo resistor
Node-Red - Introduction
Introduction to Node-Red, our flagship
Integrating Arduino in Node-Red
Using Json
Using Firmata
The Internet of Things
Introduction to MQTT
Connect to the Internet of Things

## Slide 3
https://github.com/rovale/innoexp2

## Slide 5: Arduino - Hello World
Arduino Nano
https://store.arduino.cc/usa/arduino-nano
Microcontroller ATmega328
Clock Speed 16 MHz
32 KB flash memory
2 KB SRAM
24 I/O pins
  Operating on 5V Other boards may operate on 3.3V!

## Slide 6: Arduino - Hello World
Arduino Nano
22 I/O pins
  4 functions
    20 Write digital value (1/0, HIGH/LOW)
      HIGH = 5V
      LOW = 0V
    20 Read digital value (1/0, HIGH/LOW)
      HIGH = greater than 3V
      LOW = less than 1.5V
    6 Write analog value (0 - 255), PWM
    8 Read analog value (0 - 1024)

## Slide 7: Arduino - Hello World
Prototyping
Breadboard
  https://learn.sparkfun.com/tutorials/how-to-use-a-breadboard
  Used for creating a prototype of an electronic circuit
  Power rails for + and –
  Terminal strips for connecting the components
  Support for IC's - and the Nano
  Connect components using jumper wires

## Slide 8: Arduino - Hello World
Digital output example - LED
LED
  https://learn.sparkfun.com/tutorials/light-emitting-diodes-leds
  An LED is a Light Emitting Diode
  Long leg is positive side, anode
  Short leg is negative side, cathode - has flat edge
  You can test it with a coin cell battery
  An LED will be toasted if it gets too much current
Resistor
  https://learn.sparkfun.com/tutorials/resistors
  A resistor limits the flow of electrons
  The value can be decoded using the color bands
Wiring
  Arduino pin D3 to LED to Resistor to Ground

## Slide 9: Arduino - Hello World
Programming
We got Chinese compatible Nanos here...
  Install Serial driver for Nano compatible http://www.wch.cn/download/CH341SER_EXE.html (also needed for NodeMCU V1.0)
Install Arduino IDE https://www.arduino.cc/en/main/software
Select
  Board (Arduino Nano)
  COM port (see device manager)

## Slide 10: Arduino - Hello World
Programming
01-Blink.ino
  https://github.com/rovale/Innoexp2/blob/master/Arduino/ 01-Blink/01-Blink.ino
  Written in the Arduino programming language
    https://www.arduino.cc/reference/en/
  Defines a constant with the functional name of the pin
  Has a setup and a loop
  Turns a digital pin on and off
  Uses a delay to time the blinking

## Slide 11: Arduino - Hello World
BTW…
There is also an onboard LED,
on the Arduinos it’s digital pin 13,
constant value of: LED_BUILTIN.

## Slide 12: Arduino - Advanced
Digital input example - Button
Circuit
Input pin
  Reads a random value when no input is given
Pull-up resistor
  https://learn.sparkfun.com/tutorials/ pull-up-resistors
  Puts input pin HIGH
  Prevents random inputs on the input pin
Button
  https://learn.sparkfun.com/tutorials/switch-basics
  Digital input -> HIGH / LOW
  Puts input pin LOW when pressed
Programming
02-Button.ino
  https://github.com/rovale/Innoexp2/blob/master/Arduino/02-Button/02-Button.ino
  Turns the LED on when the button is pressed.

## Slide 13: Arduino - Advanced
Analog input example - Photo resistor
Circuit
https://learn.sparkfun.com/tutorials/ photocell-hookup-guide
Light sensitive, variable resistor
More light = less resistance
  Pitch black: 1.0MΩ+
  Bright light: 0
Analog input (0 – 1024)
Programming
03-PhotoResistor.ino
  https://github.com/rovale/Innoexp2/blob/master/Arduino/03-PhotoResistor/03-PhotoResistor.ino
  Prints the measured value of a photo resistor to the serial output.
  uses a non-blocking pattern to time the print-outs.

## Slide 14: Node-Red - Introduction
https://nodered.org/docs/
This will be our flagship!
Used to wire together our Things, APIs and online services.
Used to create live data dashboards.
Originally developed by IBM and it runs on node.js.
Browser-based editor to create flows of messages and actions.
Deploy to runtime in a single-click.
It can integrate in an existing solution

## Slide 15: Integrating Arduino in Node-Red
Goal: connect the Arduino to NODE-Red and display a gauge for the light intensity and a dimmer slider for the LED.
Use Arduino as a serial device:
Using Json
  When some logic needs to be programmed on the Arduino.
Using Firmata
  When the Arduino is only used as an 'extension' to connect to the physical world.

## Slide 16: Integrating Arduino in Node-Red
Json
Arduino programming
04-Json
  Uses a library to create / parse Json messages
    https://arduinojson.org
    Libraries always come with examples.
  Uses power modulation (PWM) to dim the LED.
    https://www.arduino.cc/en/Tutorial/PWM
Node-RED programming
Flow: Arduino Serial Json
  Uses serialport nodes
    https://flows.nodered.org/node/node-red-node-serialport
  Connects the Arduino directly to the dashboard

## Slide 17: Integrating Arduino in Node-Red
Firmata
Arduino programming
Firmata
  https://github.com/firmata/protocol
  Exposes all Arduino pins on the serial port.
Node-RED programming
Flow: Arduino Firmata
  Uses Arduino nodes
    https://www.npmjs.com/package/node-red-node-arduino
  Also connects the Arduino directly to the dashboard

## Slide 18: The Internet of Things
Goal: Connect the Arduino via Node-RED to the Internet of Things using

## Slide 19: The Internet of Things
MQTT
https://www.hivemq.com/blog/mqtt-essentials-part-1-introducing-mqtt
Message Queuing Telemetry Transport
The protocol of the Internet of Things
Highlights
  Client / broker
  Publish / subscribe
  Quality of Service
  Persistent Sessions
  Retained Messages
  Last Will

## Slide 20: The Internet of Things
Publish / subscribe
A client can publish messages to a topic
  Topic: evs/innoexp2/some_device/sensor/light
  Payload: 567
A client can subscribe to topics
  One topic: evs/innoexp2/some_device/sensor/light
  Using single level wildcards: evs/innoexp2/+/sensor/light
  Using multi-level wildcards: evs/innoexp2/some_device/sensor/#

## Slide 21: The Internet of Things
Quality of Service
QoS is about the messages being sent from the client to the broker and the other way around.
QoS level 0 - At most once
QoS level 1 - At least once
QoS level 2 - Exactly once
Clients have to support it
  Microcontroller libraries go no higher than
    QoS level 0 for publishing
    QoS level 1 for subscribing

## Slide 22: The Internet of Things
Persistent Sessions
Requested when connecting
ClientId
CleanSession (false)
If the client requests a persistent session, the broker will store session information when the client goes off-line.
It stores:
The existence of a session
All subscriptions
Messages

## Slide 23: The Internet of Things
Retained Messages
Created by publishing a message with a retain flag
Will be stored by the broker till eternity
Can be deleted by publishing an empty payload
Ideal for device status messages: online / offline

## Slide 24: The Internet of Things
Last Will
Created by the client when connecting
  lastWillTopic
  lastWillMessage
  lastWillRetain
  lastWillQoS
Sent by the broker
  When a client does not respond within the Keep Alive Time
  An unexpected situation on the network
Ideal for device status message: offline

## Slide 25: The Internet of Things
Node-RED programming
Flow: Arduino MQTT
The same as the Arduino Firmata flow but now directing all communication through an MQTT broker, turning our Arduino into a 'Thing' which is connected to the Internet of Things.
This flow uses the built-in MQTT nodes.